## Slide 1
HAMADI Maoulida - TARTERA Maëlys
GT-LGT2803-Low Tech Graphite Strain Sensor
General Features:
-Low power consumption (3V-5V)
-Low cost
-Light and small (10cm2)
-Flexible and biodegradable
-Easy-to-use : plug and use
-Easily replaceable and reproductible)
-Bluetooth connection possible
Description:
The strain sensor was developed and made in the Applied Physics Department at the National Institute of Applied Sciences (INSA) of Toulouse, France.
The sensor technology is based on chemiresistor properties of graphite found in the article "Pencil Drawn Strain Gauges and Chemiresistors on Paper" published in 2014 by Cheng-Wei Lin, Zhibo Zhao, Jaemyung Kim, and Jiaxing Huang. The sensor can measure a resistance variation
This sensor consists of a small piece of paper coated with a graphite layer from a pencil. It can measure a resistance variation when applying a strain. The deformation leads to a change of the number of connected graphite particles in the thin layer of graphite and so it changes the resistance of the sensor. This allows us to measure deformation, like a traditional strain gauge.
The structure of the graphite layer varies depending on the type of pencil used. In order to fully understand the impact of the graphite structure on the variation of the resistance, we conducted tests with two types of pencils: HB (medium hardness) and 2B (softer). To achieve this, our sensors were coupled with a transimpedance amplifier and an Arduino Uno, all integrated on a PCB designed for tests.
Pin configuration and dimensions:
1

## Slide 2
Technical specifications:
Standard use conditions:
HAMADI Maoulida - TARTERA Maëlys
2
Electrical characteristics:
GT-LGT2803-Low Tech Graphite Strain Sensor
Type | Strain sensor
Materials | Graphite (4B to 2H graphite pencil)
Sensor type | Passive: Power suply required
Power supply | Vcc=+5V
Nature of output signal | Analog
Nature of measurand | Voltage
Typical response time | Less than 50 ms
Typical use | Measurement of compression deformation
Pin Number | Usage
1 | Vin
2 | +Vcc (5V)
1
2
 | Typical Value | Unit
Temperature | 20±5 | °C
Humidity | 50±5 | %
Bluetooth operation distance | 1±4 | m

## Slide 3
HAMADI Maoulida - TARTERA Maëlys
3
Typical performance characteristics:
GT-LGT2803-Low Tech Graphite Strain Sensor
Pencil type-unit of the resistance and the resistance when no strain applied
Courbes de deltaR/R0 en fonction de la deformation soit en % soit en cm

## Slide 4
HAMADI Maoulida - TARTERA Maëlys
4
GT-LGT2803-Low Tech Graphite Strain Sensor
Typical application :
The graphite strain sensor GT-LGT2803 is connected to a Vcc=5V power supply on its pin 2, its pin 1 is connected to a transimpedence amplifier circuit designed to cancel noise.
and allow the GT-LGT2803 to be connected to an

## Slide 5
HAMADI Maoulida - TARTERA Maëlys
5
GT-LGT2803-Low Tech Graphite Strain Sensor